## Slide 1: Hazardous Gases
compressed gas cylinders

## Slide 2: Hazardous gases
Toxic gases such as CO, NH3 pose risk via inhalation.
  No pressure release valves
Reactive gases like HCl, NO, and NO2 make corrosive acids in air.
Metal hydride gases such as B2H6 are highly toxic and pyrophoric.
  Decompose generating large amounts of H2 gas, over-pressurizing tanks.
  Long term storage problems.
Flammable gases– H2 and acetylene
  Lighter than air, wide flammable ranges, very low ignition (static spark)
Unstable gases decompose exothermically– acetylene, NO, NO2
Chemical asphyxiant (TOXIC)– HCN, H2S, CO
Inert gases - asphyxiate by displacing oxygen (Ar, N2, He, CO2)
  Have pressure relief valves
Non-Flammable
Gas
2
Flammable Gas
2
Inhalation
Hazard
2
Oxygen
2
Notes: Nitric oxide or nitrogen dioxide
Hydrogen disulfide

## Slide 3: Gas Cylinder Caps
Always have cylinder cap in place unless in use!

## Slide 4: Compressed Cylinders
Storage
  Secure all cylinders to a wall in designated locations using a strap.
  Labels on cylinder should be visible where stored.
    Full, in use, empty tags
  Segregate full and empty cylinders and keep incompatible cylinders >20 ft apart.
    eg oxygen gas and other flammable gasses
  Do not store cylinders >3 years.
FULL
EMPTY
IN USE
Oxygen
2

## Slide 5: Compressed Cylinders
Usage
  Get trained on the specifics of using a new regulator or gas.
  Be aware of approved regulator types, required monitors, PPE and storage when purchasing and setting up.
    (Get help from supplier eg Airgas)
  Use the buddy system when changing hazardous gas cylinders.
  Always use a proper carrier or cart with a chain.
  Do not use Teflon tape or thread sealant on cylinders.