## Slide 1: Safety Moment
Mercury

## Slide 2: Mercury Spills
Mercury bioaccumulates in humans and other animals such as aquatic life and is very dangerous to health.
If Hg is spilled make sure the area is well-ventilated
  If large spill, contact EHS for cleanup and block off the area.
  If small spill:
    Use an index card to gather droplets together, then use pipette to pick up droplets
    Place in separate properly labeled waste container
    Dispose of the waste via EHS

## Slide 3: Mercury Spills
Additional considerations:
  If spill is on the floor, put bags around feet to prevent getting Hg on your shoes
  Keep liquid Hg separate from contaminated items
    Place contaminated items (e.g. gloves) in a separate plastic bag for pickup
  Do not use a vacuum or broom – doing so can release vapors
  EHS will pick up old mercury equipment like thermometers and bubblers to keep mercury devices out of the department.